## Slide 1: Customer topology use case

## Slide 2: Motivation of a customer for expressing topology intents
Build the logical view of the desired slice service (and its parts)
  Impact on realization -> hints for the NSC on how to instantiate the slice service
Operate the slice service according to the expressed topology
  Impact on control of the slice -> out of scope

## Slide 3: IETF Network Slice Connectivity Constructs
IETF Network Slice Service (NS1) consist of four Connectivity matrices with 4 different SLAs Blue, Red and Green
SDP1
SDP2
SDP3
SDP7
SDP6
Type Any-to-any
connectivity-matrix-id =Blue
Key=Blue
Type P2P
connectivity-matrix-id = Orange
Key= Orange
SDP5
SDP9
SDP10
Type P2MP
connectivity-matrix-id = Green
Key=Green
Modelling as NS framework definition
  This is what is currently in the framework draft!
  Multiple connection matrices
  SLO of each connection is different
  Each CM is one entry (i.e., connection)
    CM Blue: Src{1,2,6} Dst{1,2,6} with SLO Blue
    CM Orange: Src{3} Dst{7} with SLO Orange
    CM Red: Src{7} Dst{6} with SLO Red
    CM Green: Src{5} Dst {9,10} with SLO Green
  Connectivity matrix Key = {new connectivity-matrix-id} (i.e. Blue, Orange, Red, Green)
    Note: connection type is not part of the key
Type P2P
connectivity-matrix-id = Red
Key=Red

## Slide 4: Example
SDP1
SDP2
SDP3
SDP7
SDP6
Type Any-to-any
connectivity-matrix-id =Blue
Key=Blue
Type P2P
connectivity-matrix-id = Orange
Key= Orange
DU
CU
UPF
DU
SDP1
SDP2
SDP6
SDP3
SDP7
A
C
D
B
SDP1
SDP2
SDP6
SDP3
SDP7
w/o customer topo
With customer topo
Notes: Resource reservation based on network planning (forcast of the demand traffic matrix)
- points of SAP (service access point) -- APs in ACTN VN
- customer has a forcast of demand traffic matrix between the SAPs to which the customer can be connected

## Slide 5: Motivation of a customer for expressing topology intents
Using customized topologies for resource reservation and sharing
  Make sure resources are reserved between SDPs when connections are requested
    Connections are configured on demand by customer, and no pre-defined schedules for the customer. This scenario cannot be satisfied by connectivity-based network slices because there is no guarantee of resource availability when a new connection is requested
  Resources can be shared between different connections in the same connectivity construct
    For connectivity-based network slices the bandwidth is dedicated for each connection

## Slide 6: Build Customized Topologies
A SAP topology is required to be exposed by the NS provider prior to NS configurations
  List of SAPs
A customized topology is built by a customer using the SAP topology information. It may contain:
  Edge Node – represents CE devices connected to one or multiple SAPs
  Intermediate Node (P-node) – a virtual node abstraction not associated with any SAPs, is used to express topological constraints such as resiliency and load-balancing
  Link – connecting the above nodes to form possible e2e path. Link can carry SLO attributes such as bandwidth and latency

## Slide 7: Example
Network Slice request between DU1/2 and CU
DU3 – CU is planned for future expansion
DU1
CU
DU2
SDP1
SDP2
SDP6
DU3
SDP3

## Slide 8: Option 1 : Connectivity-based Network Slice
Two dedicated connections upfront with 10G per connection = 20G total bandwidth used
When DU3 needs to connect to CU – a new connection is requested & added to the conn. Construct
There is no guarantee that DU3-CU connection can be created due to unavailable resources
Bandwidth is not shared between (DU1,DU2,DU3)
DU1
CU
DU2
SDP1
SDP2
SDP6
DU3
SDP3
SDP1
SDP2
SDP6
10G
10G
SDP3
Type P2P
connectivity-construct-id =Blue
Key=Blue
10G

## Slide 9: Option 2 : Customized Topology with Edge Node and Dedicated Link
Customized topology with dedicated link between DU1/DU2/DU3 and CU for resource reservation, no bandwidth sharing between (DU1, DU2, DU3)
Connection 1 and 2 can be created subsequently
Connection 3 may be added later on demand
DU1
CU
DU2
SDP1
SDP2
SDP6
DU3
SDP3
DU3
DU1
DU2
CU
10G
10G
10G
Conn. 2
Conn. 1
Conn. 3

## Slide 10: Option 3 : Customized Topology with Edge Virtual Node and Shared Bandwidth
Customized topology with a single virtual node representing DU1-DU3, and a shared link between DU1/DU2/DU3 and CU for resource reservation
Bandwidth is shared between (DU1, DU2, DU3) with less bandwidth (20G vs. 30G) reserved
Connection 1 and 2 can be created subsequently
Connection 3 may be added later on demand
DU1
CU
DU2
SDP1
SDP2
SDP6
DU3
SDP3
DU1-3 Virtual Node
3
1
2
CU
20G
Conn. 1
Conn. 2
Conn. 3

## Slide 11: Option 3 : Customized Topology with Intermediate Node
Customized topology with edge nodes representing DU1-DU3, two P nodes to express load balancing and protection between each DU and CU
Bandwidth is shared between (DU1, DU2, DU3) with less bandwidth (20G vs. 30G) reserved
Connection 1 and 2 can be created subsequently
Connection 3 may be added later on demand
DU1
CU
DU2
SDP1
SDP2
SDP6
DU3
SDP3
DU3
DU1
DU2
P-node1
CU
10G
10G
10G
10G
P-node2
10G
Conn. 1
Conn. 2
Conn. 3

## Slide 12: Backup Slides

## Slide 13: Option 1: Customized Topology with dedicated
DU1
DU2
DU3
CU
SAP1-3 Virtual Node
1
2
3
SAP4
10G
10G
10G
20G
SAP1
SAP2
SAP3
P-node
SAP4
20G
10G
10G
10G
P2-node
Notes: Resource reservation based on network planning (forcast of the demand traffic matrix)
- points of SAP (service access point) -- APs in ACTN VN
- customer has a forcast of demand traffic matrix between the SAPs to which the customer can be connected
- schedule is not known a prior
Using topologies to express customer constraints on:
Resiliency
Load-balancing

## Slide 14: Example
Traffic must follow route DU –> CU –> UPF
DU3 – CU is planned for future expansion
CU-UPF bandwidth is shared regardless of how many DUs are connected
DU1
CU
UPF
DU2
SDP1
SDP2
SDP6
SDP3
SDP7
DU3
SDP3