## Slide 1: IETF Network Slice Topology YANG Data Model
Co-authors:
Xufeng Liu (Alef Edge)
Jeff Tantsura (Microsoft)
Igor Bryskin (Individual)
Luis M. Contreras (Telefonica)
Qin Wu (Huawei)
draft-liu-teas-transport-network-slice-yang-07
Sergio Belotti (Nokia)
Reza Rokui (Ciena)
Aihua Guo (Futurewei)
Italo Busi (Huawei)

## Slide 2: Motivation of a customer for expressing topology intents
Build the logical view of the desired slice service (and its parts)
  Impact on realization -> hints for the NSC on how to instantiate the slice service
Operate the slice service according to the expressed topology
  Impact on control of the slice -> out of scope

## Slide 3: Similar Requirements in ACTN VN Type 2
TODO – add ACTN VN Type 2 description (Italo)

## Slide 4: Feedbacks on NS Topology
Proposed use case is not convincing to explore using topologies for network slicing
  Presenting additional use case from a provider’s perspective
There are still concerns in the concept of a customized topology
  Whether building a customized topology require prior topology information from the provider
  How the NSC may map a customized topology to an internal realization, e.g. an NRP
  Whether the constraints expressed by a customized topology can be instead expressed by the connectivity constructs
  Whether existing models are sufficient to express a customized topology

## Slide 5: Addressing WG Concerns
Whether building a customized topology require prior topology information from the provider
  It’s not mandatory but a customized topology may be built using e.g. a SAP topology exposed by the provider (RFC9408)
How the NSC may map a customized topology to an internal realization, e.g. an NRP
  Edge node – PE node attached to a SAP
  Edge TP – SDP
  Transit node (P-node) – translated to resource sharing constraints
  Link – reserved resources
Whether the constraints expressed by a customized topology can be instead expressed by the connectivity constructs
  We show by the use case that in some scenarios it is more efficient to use topologies to express the constraints, e.g. diversities, resource sharing
Whether existing models are sufficient to express a customized topology
  Base model exists (RFC8345 network topology)
  No suitable model exist to express topology + SLO/SLE

## Slide 6: IETF Network Slice Connectivity Constructs
IETF Network Slice Service (NS1) consist of four Connectivity constructs with 4 different SLAs Blue, Red and Green
SDP1
SDP2
SDP3
SDP7
SDP6
Type Any-to-any
connectivity-construct-id =Blue
Key=Blue
Type P2P
connectivity-construct-id = Orange
Key= Orange
SDP5
SDP9
SDP10
Type P2MP
connectivity-construct-id = Green
Key=Green
Modelling as NS framework definition
  This is what is currently in the framework draft!
  Multiple connection matrices
  SLO of each connection is different
  Each CC is one entry (i.e., connection)
    CC Blue: Src{1,2,6} Dst{1,2,6} with SLO Blue
    CC Orange: Src{3} Dst{7} with SLO Orange
    CC Red: Src{7} Dst{6} with SLO Red
    CC Green: Src{5} Dst {9,10} with SLO Green
  Connectivity construct Key = {new connectivity-construct-id} (i.e. Blue, Orange, Red, Green)
    Note: connection type is not part of the key
Type P2P
connectivityconstruct-id = Red
Key=Red

## Slide 7: Example
Resources may be allocated in the same NRP w/o customer topology
Adding DU nodes could affect the CU-UPF connections
SDP1
SDP2
SDP3
SDP7
SDP6
Type Any-to-any
connectivity-construct-id =Blue
Key=Blue
Type P2P
connectivity-construct-id = Orange
Key= Orange
DU
CU
UPF
DU
SDP1
SDP2
SDP6
SDP3
SDP7
A
C
D
B
SDP1
SDP2
SDP6
SDP3
SDP7
w/o customer topo
With customer topo
Resource isolation and resource reservation between DU-CU and CU-UPF based on network planning using forecast of demand traffic matrix
On-demand addition of DU-CU connections based on planning
Notes: Resource reservation based on network planning (forcast of the demand traffic matrix)
- points of SAP (service access point) -- APs in ACTN VN
- customer has a forcast of demand traffic matrix between the SAPs to which the customer can be connected

## Slide 8: Next Steps
Address comments / questions
Request for WG adoption
* GitHub Repo
  https://github.com/aguoietf/ietf-network-slice-topology

## Slide 9
Thank You!