## Slide 1: IETF Network Slice Topology YANG Data Model
Co-authors:
Xufeng Liu (Alef Edge)
Jeff Tantsura (Microsoft)
Igor Bryskin (Individual)
Luis M. Contreras (Telefonica)
Qin Wu (Huawei)
draft-liu-teas-transport-network-slice-yang-07
Sergio Belotti (Nokia)
Reza Rokui (Ciena)
Aihua Guo (Futurewei)
Italo Busi (Huawei)

## Slide 2: Motivation
A network slice customer may request an additional level of control to customize the service paths in a network slice (Sec. 2 of draft-ietf-teas-ietf-network-slices)
In some use cases, a customer may ask for shared instead of dedicated resources to save cost
  Resources are reserved ahead but not activated
  Connections can be activated on demand
Current NS NBI model only addresses connectivity-based network slicing
  Dedicated connections with resources allocated for each connection
  To request resource sharing, on-demand reconfiguration of connections is needed but there is no guarantee that resources are always available at the time of request
Customized topology can help -
  Customer can express some level of customized control: explicit path, diversity, protection/restoration, etc.
  A customized topology can encode resource reservation request to secure the resources
  Allows customer to use resources to create and reconfigure network slice connections in a flexible way
And it’s complementary!
  Optional extension to support resource reservation in addition to connectivity-based slicing

## Slide 3: Terminologies
Customized Topology: A topology defined by the customer and served as an input to the network slice service provider, i.e. to the Network Slice Controller (NSC). (In scope)
Abstract Topology: A topology exposed to the customer by the network slice service provider prior to the creation of network slices. (Out of scope)
NRP Topology: A topology internal to the NSC to facilitate the mapping of network slices to underlying network resources. (Out of scope)

## Slide 4: Some History with This Draft
(-00 to -05) of the draft was positioned as an alternative model for network slicing NBI
  Provider may expose an abstract topology using this model
  Customer may define a network slice as a customized topology using the same model
(-06 and -07) of the draft re-positioned the draft
  As a complementary data model for resource-based network slices (reserve and activate)
  Only used by the customer to define customized topologies

## Slide 5: An Example Scenario
Network Slice Request: multiple stadiums share one 100G HD broadcast channel to the TV station
Alternating use of bandwidth between the stadiums (no parallel TV broadcast events on the same day)
Bandwidth must be available at the time of request
No pre-defined schedule (or ad-hoc events) with the broadcast
PE1
PE2
PE3
PE4
Stadium 1
Stadium 2
Stadium 3
TV Station
Option 1
  Created NS with dedicated connections (s1-t, s2-t, s3-t)
  Pay for 3x needed bandwidth
Option 2
  Created NS with one connection (s1-t)
  Dynamically reconfigure the NS connection to connect one stadium with the TV station
  Bandwidth may not be available at the time of reconfiguration
P1
P2

## Slide 6: An Example Scenario (Cont.)
Network Slice Request: multiple stadiums share one 100G HD broadcast channel to the TV station
Alternating use of bandwidth between the stadiums (no parallel TV broadcast events on the same day)
Bandwidth must be available at the time of request
No pre-defined schedule (or ad-hoc events) with the broadcast
PE1
PE2
PE3
PE4
Stadium 1
Stadium 2
Stadium 3
TV Station
Option 3
  Create a customized topology with two nodes and one 100G link
    vPE1 represents an abstracted view of the 3 stadiums
    vPE2 represents the TV station
  Pay only 1x 100G bandwidth
  Resources are reserved in advance
  Customer can dynamically create/remove connections
  Of course, the NSC will need to support the resource reservation (part of SLO/SLE for the topology)
  More fine-grained control can be expressed
    Use P node to describe route preferences (e.g. geo-location)
    Multi-path protection & restoration
P1
P2
vPE1
vPE2

## Slide 7: How does a Customer Understand a Customized Topology?
Customized topology is defined in the customer context, may not be understood by the provider. Provider needs to translate a customized topology an internal realization (e.g. mapped to an NRP)
There are a few options…
  Associate a SAP/SDP with a TP in the customized topology
  Use the same id between the customer and provider
  What about P-nodes in a customized topology?
    The customized topology can be as simple as PE nodes + links, so a P-node is completely optional
    A P-node may be used to represent a policy node, e.g. a geo location over which a service path must (or must not) traverse
Another option is to expose an abstract topology
  Does not apply to all providers due to security / data privacy consideration
  However, if exposed, such an abstract topology could help the provider to advertise its capabilities to the customer
    Mechanism to expose an abstract topology is outside the scope of this draft
    E.g. with an augment of RFC9408, or RFC8795 (TE topology)

## Slide 8: Updates to draft -07
Text updates to clarify the use of customized topology and address comments received from the WG
Moved augments for adding service paths over NS connections from draft-ietf-ccamp-otn-slicing to this draft

## Slide 9: Open issue
Currently, draft-ietf-teas-ietf-network-slice-nbi-yang has a reference to a customized topology without specifying how to use it
Shall we move the above reference to this draft?
  Clear separation of modeling: ns-nbi focuses only on connection-based network slicing, while this draft provides resource-based slicing with definitions to a customized topology and usage of such a topology

## Slide 10: Next Steps
Request for WG adoption
Resolve open issues
* GitHub Repo
  https://github.com/aguoietf/ietf-network-slice-topology

## Slide 11
Thank You!